## Slide 1: BIG Power BIG Aperture small satellite
Mark Bailey
Director of Business Development, MMA Design
mbailey@mmadesignllc.com
303-877-4119

## Slide 2: High Watts per Kilogram (HaWK) Solar Arrays
GSFC Planetary CubeSats Symposium 2018
Aug. 16-17, 2018

## Slide 3: MMA’s “HaWK” Solar Arrays
MMA has been providing solar arrays for CubeSats over 10 years
Focus on “High Watts per Kilogram” (HaWK) and packing efficiency (Watts per m³)
Power requirements have ranged from 42 W (3U) to 220+ (16U) Watts
Single-axis SADA available for 1U- and 2U-width buses
  Supports 3U, 6U, 12U, and 16U satellites
GSFC Planetary CubeSats Symposium 2018
Aug. 16-17, 2018

## Slide 4: High Performance & Reliability
Packaging to maximize power in any CubeSat deployer
Current state-of-production cells from the best heritage suppliers
Welded strings for thermal extremes and longer life
Robust mechanisms
Rigid Panels/High 1st mode Frequency
Proven workmanship
Optional 1 axis SADA
  1U Package for 3U/6U
  2U package for 6U/12U
  Standard or High Power models
GSFC Planetary CubeSats Symposium 2018
Aug. 16-17, 2018

## Slide 5: HaWK Array Heritage 100% Success Rate
GSFC Planetary CubeSats Symposium 2018
Aug. 16-17, 2018

## Slide 6: Pushing Performance
MMA is currently advancing CubeSat Power to new levels with support from an Air Force SBIR Phase II grant.
Technology/Performance Advances
~200+ watts in a 6U/12U package
XL Power 1 axis SADA
Increased voltage options as small as CubeSats 28-100V+
  Enables direct-drive power for SEP Thrusters
GSFC Planetary CubeSats Symposium 2018
Aug. 16-17, 2018

## Slide 7: Advanced Packaging Approach for SmallSat Solar Arrays
MMA’s rHaWK technology is targeted for ESPA-class small satellites and larger
Architecture is efficient at power levels greater than 500 watts, and up to multiple kilowatts
Concept combines features of MMA’s lightweight HaWK solar panels and deployable tape-boom technologies (high TRL)
Multiple HaWK panels and deployable side panels are deployed and supported by a deployable tape-spring truss
The assembly can be attached to a SADA
2 kW ESPA Array
(BOL, AM0, 28°C)
24x28x36 inch ESPA Bus
Nanosat Truss
HaWK Panels
Typical high-performance array targets: 120 W/kg, 40kW/m3
rHaWK: 130+ W/kg, ~93 kW/m3
GSFC Planetary CubeSats Symposium 2018
Aug. 16-17, 2018

## Slide 8: 1 kW rHaWK Wing
[3.66 m]
144 in
[1.24 m]
49 in
Bus Interface
[300 mm]
12.0 in
HaWK panels attach to boom at every other hingeline
GSFC Planetary CubeSats Symposium 2018
Aug. 16-17, 2018

## Slide 9: Comparison to Tensioned Blanket
The rHaWK architecture is similar to tensioned-blanket arrays but offers the following benefits and advantages:
  Array does not require tension, relaxing the stiffness and strength requirements (and mass) of the boom
  Array has a reduced effective length (multiple attach points along the length), increasing the first mode compared to a blanket that is attached only at the tip and root.
  Rigid substrates offer improved radiation shielding and thermal management over flexible blanket substrates
  MMA boom does not use a canister (better mass and packaging efficiency, W/kg & kW/m³)
  Stowed form factor is more friendly and flexible for SmallSats and small launch vehicles
    Array stows as a rectangular stack of rigid panels
    Boom does not require a deployment canister
GSFC Planetary CubeSats Symposium 2018
Aug. 16-17, 2018

## Slide 10: Frequency Specific MMA Deployable High-Gain Reflectarray (DaHGR) (1U+)
GSFC Planetary CubeSats Symposium 2018
Aug. 16-17, 2018

## Slide 11: Deployable High Gain Reflectarray (DaHGR)
  Patent-pending designs create reflectarray on thin film membranes
    Leverages high TRL design elements
      TRL-9 dragNET De-orbit System and launch restraints
      TRL-8 FalconSAT-7 diffractive optical membrane
        TRL-9 in 2018
      Flight heritage composite tapes
        Full tape deployer at TRL-9 in 2018/19
    Efficiency comparable to rigid reflectors (~60%)
    Frequencies up to Ka-Band
      Possibly higher, aperture dependent
    Membrane Reflectarray technology allows flat/planar surfaces instead of parabolic/curved, trading large bandwidth for reduced complexity
P- DaHGR Antenna Architecture (patent pending)
T-DaHGR Antenna
(patent pending)
GSFC Planetary CubeSats Symposium 2018
Aug. 16-17, 2018

## Slide 12: T-DaHGR Overview
UHF–Ka band
High stiffness
Low RF losses
  Equivalent to conventional reflectors
Up to 20+% bandwidth
Thermally stable
1 – 20 m aperture
0.5 - 1.00 m2/U packing efficiency
1U – 25U volume
GSFC Planetary CubeSats Symposium 2018
Aug. 16-17, 2018

## Slide 13: Top Level System Working Requirements
Parameter | Estimated Performance
Mass (kg) | ≤ 2
Stowed Volume (mm) | 100 x 100 x 100
Deployment Duration (sec) | < 600
Active Aperture Area | ≥ 1 meter diameter
Center Frequency (GHz) | 8.2 - 8.45
Gain (dBi) | > 35
Beamwidth (degrees) | 2.3
Bandwidth (MHz) | > 10%
Return Loss | < 2:1 VSWR
T-DaHGR System
GSFC Planetary CubeSats Symposium 2018
Aug. 16-17, 2018

## Slide 14: T-DaHGR System Overview
Stowed
Restraint door released
Deployed
Primary Reflectarray Membrane
(Active RF Area ~ 1M diameter)
100 mm
100 mm
100 mm
Secondary Reflectarray Membrane
RF Feed
GSFC Planetary CubeSats Symposium 2018
Aug. 16-17, 2018

## Slide 15
Experiment Technical Information
Apogee: 550 nominal +/- 50 km
Perigee: 550 nominal +/- 50 km
Inclination: 55 nominal
Mass: 10.67 kg
Dimensions: 11 x 23 x 36 cm
Power: 28 W
Sponsor: AFRL
End Users: DoD, NASA, NOAA, Commercial SmallSat
Experiment Type: Comm
Flight Ready Date: September 2020
Objective
  Demonstrate High Data Rate Downlink and Uplink Capabilities in small SWaP Form Factor
  Demonstrate Code Division Multiple Access (CDMA) Downlink and Uplink
  Characterize the MMA T-DaHGR deployable X-Band antenna on-orbit performance
  Characterize the Chip Scale Atomic Clock (CSAC) on-orbit performance
  Tech Transition
  High data rate comm capabilities for use in SmallSat community
  Spread spectrum CDMA capabilities for use in SmallSat community
  High gain 1U deployable antenna for use in SmallSat community
  Advancement in high rate communication technology of interest to cutting edge industry leaders within the SmallSat community
MAXWELL fully deployed with MMA antenna
GSFC Planetary CubeSats Symposium 2018
Aug. 16-17, 2018

## Slide 16: DaHGR Options
GSFC Planetary CubeSats Symposium 2018
Aug. 16-17, 2018

## Slide 17: Conclusions
MMA HaWK Arrays offer several benefits to interplanetary missions:
  Exceptional packaging efficiency
  State-of-the-art for power density at up to 130 W/kg
  High reliability, industry-heritage rigid-panel array materials and processes
  Rigid substrates offer radiation shielding and thermal stability for long-duration and deep space missions
  Options for structural depth offer high stiffness and strength for delta-v maneuvers
    Canister-free, linearly-deploying boom structure is available for deploying or supporting other sensors
  Scalable architecture enables 220+ watts on CubeSats and 6+ kW on ESPA buses
GSFC Planetary CubeSats Symposium 2018
Aug. 16-17, 2018

## Slide 18: Conclusions
MMA DaHGR offers several benefits to interplanetary missions:
  Exceptional packaging efficiency
  Demonstrating X Band gain at 35+ dBi; gain
  Potential for implementation up to Ka Band with increased gain
  High reliability, industry-heritage materials and processes
  Alternative configuration options
    Cassegrain T-DaHGR - ready for flight by 2019
    Pantograph P-DaHGR - qualified and delivered, flight in 2018/19
    Direct fed off-axis T-DaHGR – completed CDR
    Transmissive Lens – conceptual design proposed for 2019 funding
    Rigid Substrate (R-DaHGR) – funded for TRL advancement
  Scalable architecture enabling 1 m2 on a CubeSat up to 50+ m2 on an ESPA Grande bus
GSFC Planetary CubeSats Symposium 2018
Aug. 16-17, 2018

## Slide 19
Delivering Innovative Deployable Solutions
GSFC Planetary CubeSats Symposium 2018
Aug. 16-17, 2018