## Slide 1: DellingrX: System Development Progress to Date
Charles Clagett
6/28/2019
charles.e.clagett@nasa.gov
301-286-2438
National Aeronautics and Space Administration
www.nasa.gov

## Slide 2: DellingrX Systems to Meet Unique Space and Planetary Science Goals
Spacecraft bus architecture designed for higher reliability and harsh environments
System architecture and design to enable space and planetary missions with harsh environments proposed by our scientists
Spacecraft bus designed to support a wide variety of mission concepts:
  Hitchhiker with primary spacecraft for transportation but independent operations
  Daughtership with primary spacecraft for transportation, communications, and occasional navigation
  Free Flyer after LV separation
  Probe/Lander/Penetrator interacting with planetary body deemed too risky for primary spacecraft
Balances and scales programmatic and technical risks for Class-D mission:
  Safety and mission assurance, parts selection, GOLD rules, design margins, and testing
Reduces SWaP by merging subsystems together while increasing flexibility and robustness

## Slide 3: DellingrX – System Engineering Development to Address SmallSat Mission Challenges and Status
Planetary/Harsh SmallSat Mission Challenges | 
Radiation | Surviving and performing in high radiation environments
Lifetime | Surviving long duration cruises or mission profiles Achieving higher reliability
Power | Generating solar power beyond 1 AU and increasing capability for communications and propulsion
Mechanical/Thermal | Design customization for unique mission req’s
DellingrX Capability
No destructive SEE < 37MeV/cm2, piece part minimum TID > 30krad, system TID with part upgrades and shielding >100krad Other SEE monitored and mitigated (frequency is orbit dependent but analyzable and below typical nuisance threshold)
Reliability analysis and screening of critical parts Robust fault tolerance increasing overall system resiliency and enabling grateful degradation
Current design with 50W-250W input power @ 1AU, BOL, 85% efficient. Secondary voltages +12V (3A), +5V (5A), +3.3V (3A), unregulated bus ~+12V or +28V (10A) Configurable power distribution with 8 switched channels (4 latching current limited) scalable to 16 Watchdogs, commandable resets
Core system development

## Slide 4: DellingrX – System Engineering Development to Address SmallSat Mission Challenges and Status (continued)
Planetary/Harsh SmallSat Mission Challenges | 
Communications | Closing Direct to Earth (DTE) links over large distances, and crosslinks to relay mothership
C&DH | Reduce SWaP by merging subsystems while increasing flexibility and robustness
GN&C | Tracking and navigating outside GPS, desaturating wheels, and common configurable platforms for spin-axis and 3-axis stabilized spacecraft
Propulsion | Increasing delta-V for orbit insertions and exploration/orbit maintenance
DellingrX Capability
Compatibility with IRIS radio S-band development for use with NEN and SN
Real time processing subsystem Softcore LEON3FT in an RTG4 FPGA Running Core Flight System (cFS) Software Optional High Performance processing node add-on Xilinx Ultrascale+ FPGA High performance onboard data processing Many digital, analog, telemetry interfaces (covers many standard components) Supervisory monitors and watchdogs
Optical navigation in development for deep space communication and navigation support Pointing knowledge of 18 arcsec (1 sigma) with start tracker output at >4Hz and autonomous keep-out zone implementation Pointing accuracy <1 deg
Compatible with most of the mature Smallsat propulsion systems

## Slide 5: DellingrX – Simplified System Architecture
Planned performance enables a significant portion of planetary missions while balancing cost

## Slide 6: DellingrX - Development Status and Schedule
Completed System Requirement Review/System Design Review – 11/2018
  Common mission req’s and preliminary design with input from 4 science communities
Designed tiered approach for system functional reliability, reducing cost of non-critical components
Identified trade studies and capabilities gaps
Baselined communications architecture
In layout for both C&DH and high performance processor cards
Testing performance and reliability of several ADCS components for infusion in the baseline
Future High Level Milestones
  Bus core EDU components available (TRL 5) – 1/2020
  Core subsystems ETU design reviews: through 3/2020
  Flight of C&DH subsystem will occur in GTOsat – 3/2021

## Slide 7: Contacts and Acronyms
Charles Clagett – DellingrX Project Manager
  charles.e.clagett@nasa.gov
  301.286.2438
Luis Santos – DellingrX System Engineer
  luis.h.santos@nasa.gov
  301.286.5381
Michael Johnson – ETD Chief Technologist
  michael.a.johnson@nasa.gov
  301.286.5386
Larry Kepko – SSPO Chief Scientist
  larry.kepko@nasa.gov
  301.286.2728
ADCS – Attitude Determination & Control System
ETD - Engineering & Technology Directorate
AU – Astronomical Unit
C&DH – Command and Data Handling
cFE/cFS – core Flight Executive/core Flight Software
COTS – Commercial Off the Shelf
FPGA – Field Programmable Gate Array
GN&C – Guidance, Navigation, & Control
GPS – Global Positioning System
GSFC – Goddard Space Flight Center
GTO – Geostationary Transfer Orbit
LEO – Low Earth Orbit
NEN – Near Earth Network
PSE – Power Supply Electronics
RWA – Reaction Wheel Assembly
SEE – Single Event Effects
SN - Space Network
TRL – Technology Readiness Level